ECE 4723: Embedded Systems
Spring 2019

Lab 2
ESOS and the ECE 4723/6723 Target Board

Authors:
Christian Bush, Spencer Callicott, Will Carroll,
Landon Casey, Jack Fletcher

{cbb330, sc2257, woc17, lec426, jdf469}@msstate.edu

1/26/2019
Board Assembly Procedure
STEP 1: Power
LM2937
- Solder three terminals, as well as the heat sink to the heat plate pads on the reverse side.
- Check continuity between heat plate and the heat sink using a multimeter with probes between the heat plates on the reverse side and the heat sink on the chip.
- Confirm that pin 1 of the chip is connected to pad C of the JP1 pin junction.
C6
- Solder on 0.1uF capacitor.
- Check continuity between positive pad between C6 and pad C of JP1.
- Check continuity between negative pad between C6 and ground.
C7
- Solder on 10uF capacitor.
- Check continuity between positive pad of C7 and pin 3 of LM2937.
- Check continuity between negative pad of C7 and ground.
R1
- Solder on 1.5k Ohm resistor.
- Check continuity between pin 3 of LSM2937 to input of R1.
3.3V Power LED
- Discover cathode pad for LED by using continuity test between the pads and ground.
- Solder on Green LED.
- Check continuity between anode of LED and output of R1.
C1, C2, C3, C4, C5
- Check continuity between all input pads and 3.3V.
- Check continuity between all output pads and ground.
STEP 2: MCU
dsPIC33EP512GP806
- Ensure the circle in the MCU is placed over the circle printed on the PCB.
- Ensure that all footprints line up on the PCB, and solder the MCU.

STEP 3: MCU Output LEDs
LED1
- Discover cathode pad for LED by using continuity test between the pads and ground.
- Solder on Red LED.
- Check continuity between anode of LED and output pad of R2
LED2
- Discover cathode pad for LED by using continuity test between the pads and ground.
- Solder on Yellow LED.
- Check continuity between anode of LED and output pad of R3
LED3
- Discover anode pad for LED by using continuity test between the pads and output pad of R4.
- Solder on Green LED.
- Check continuity between cathode of LED and input to MCU LED3 signal.
R2
- Solder on 1.5k Ohm resistor.
- Check continuity between input of resistor and output of MCU LED1 signal.
- Check continuity between output of resistor and cathode of LED1.
R3
- Solder on 1.5k Ohm resistor.
- Check continuity between input of resistor and output of MCU LED1 signal.
- Check continuity between output of resistor and cathode of LED2.
R4
- Solder on 1.5k Ohm resistor.
- Check continuity between input of resistor and 3.3V.
- Check continuity between output of resistor and cathode of LED3.
STEP 4: MCU Serial Connection to PC (FTDI - MCU)
FTDI
- Cut 6 pins off of the 40 pin part in the kit.
- Solder on the 6 pin header.
- Check continuity between MCUTX and MCURX pin headers (4,5) and MCUTX and MCURX pins on MCU.
- Check continuity between USB5V pin header and JB1 pad 1.
- Check continuity between Ground pin header and ground.
STEP 5: MCU Programming (ICSP)
SV1
- Cut 6 pins off of the 40 pin part in the kit.
- Solder on the 6 pin header.
- Check continuity between MCLR, VICP, PGED, PGEC, and PGLVP pin headers (1,2,4,5,6) and their respective pins on the MCU.
- Check continuity between Ground pin header and ground.
STEP 6: MCU Inputs (SW1, SW2, SW3, RPG1, and POT)
SW1
- Discover correct input of SW1 by testing continuity between SW1 MCU pin and pads of SW1 footprint.
- Solder the SPST switch.
- Check continuity between the output of SW1 and ground.
SW2
- Discover correct input of SW2 by testing continuity between SW2 MCU pin and pads of SW2 footprint.
- Solder the SPST switch.
- Check continuity between the output of SW2 and ground.
RESET switch
- Solder on SPST switch.
- Check continuity between output of R0 and input of switch.
- Check continuity between switch and ground.
C0
- Solder on 10uF capacitor.
- Check continuity between VCAP output on MCU and input of C0
- Check continuity between VCAP MCU pin and pads of C0 footprint.
- Check continuity between output of C0 and ground.
R0
- Solder on 10k Ohm resistor.
- Check continuity between output of R0 and RESET switch footprint.
Check continuity between 3.3V MCU pin and pads of R0 footprint.
S0
- Solder the rotary encoder.
- Check continuity between the SW3 pad and the SW3 MCU pin.
- Check continuity between RPGA/B pads and the RPGA/B MCU pins.
- Check continuity between ground pad and ground.
POT
- Solder potentiometer.
- Check continuity between 3.3V footprint pad and 3.3V.
- Check continuity between VPOT footprint pad and VPOT MCU pin.
- Check continuity between ground footprint pad and ground.